## Slide 1: SpiderBat: Augmenting Wireless Sensor Networks with Distance and Angle Information
Georg Oberholzer, Philipp Sommer, Roger Wattenhofer

## Slide 2: Location in Wireless Sensor Networks
Context of sensor readings
  <location, time, value>
Leverage location information
  Network layer: geographic routing
  Physical layer: transmission power control
Learn about the current node position
  Nodes might be attached to moving objects
Alice
Bob

## Slide 3: Learning the Position of Sensor Nodes
Global Positioning System (GPS)
  Not for indoor applications
  Special hardware required
  High power consumption
Radio-based (connectivity/signal strength)
  High node density required
  Limited accuracy (multipath effects)

## Slide 4: Positioning with Ultrasound
Inspired by nature ...
Human hearing range: 20 – 20,000 Hz
20 – 120,000 Hz

## Slide 5: Ultrasound meets Sensor Networks
High accuracy
  Speed of sound c = 343 m/s
Low complexity
  Simple analog circuits for signal processing and peak detection
Energy efficiency
  Short pulses (e.g. 250 microseconds)
  Duty-cycling ultrasound transmitter/receivers
 | TelosB/Tmote Sky | MicaZ/IRIS
Clock speed | 32 kHz | 1 MHz
Resolution | 1.04 cm | 0.343 mm

## Slide 6: Related Work
[Priyantha et al., 2000]
Cricket
[Whitehouse et al., 2004]
Calamari
[Savvides et al., 2001]
Medusa

## Slide 7: Ultrasound Ranging
Time difference of arrival (TDoA) between radio and ultrasound:
  Radio packet wakes up ultrasound receivers
  Ultrasound pulse is sent after a constant delay
Sender
Receiver
t

## Slide 8: Distance based Positioning in Sensor Networks
Determine position based on distances to anchor nodes (trilateration)
3 anchor nodes

## Slide 9: Positioning in Sparse Networks
How does angle information help to position nodes?
1 anchor node
3 anchor nodes

## Slide 10: The SpiderBat Ultrasound Platform
4x Ultrasound Receivers @ 40 kHz
4x Ultrasound Transmitters @ 40 kHz
Digital Compass
6.5 cm (2.56 inches)

## Slide 11: System Architecture
SpiderBat is an extension board for wireless sensor nodes

## Slide 12: Ultrasound Receiver Circuits
Three amplification stages with a total gain of 58-75 dB
Each receiver provides two output signals:
  Digital comparator output generates an interrupt signal (RX_INT)
  Analog signal output (RX_ADC)

## Slide 13: Experimental Evaluation
Prototype Hardware
  SpiderBat extension board
  Atmel ZigBit900 (Atmega1281 MCU + RF212 radio)
Software
  Ultrasound ranging application implemented in TinyOS 2.1
  Distance/angle/compass information forwarded to a base station

## Slide 14: Accuracy of Distance Measurements
Measurement errors are in the order of a few millimeters
  Std. dev of error is 5.39 mm (0.21 inch) at 14 m (45.9 feet)

## Slide 15: Angle-of-Arrival Measurements with SpiderBat
Receiver
Sender
North
East
South
West
Tn
Te,Tw
Ts

## Slide 16: Angle-of-Arrival Estimation
We can calculate the angle based on the TDoA at the receivers

## Slide 17: Accuracy of Angle Measurements
Estimation of the angle-of-arrival within a few degrees
  Error is less than 5° for short distances between sender and receiver

## Slide 18: Indoor Experiments
4 nodes placed in a gym hall, single anchor node (Node 1)
200 measurements for each node
Std. dev. < 15.5 cm (6.1 inch)
Step 1: Distance + angle to nearest neighbor
Anchor
Std. dev. < 5.7 cm (2.2 inch)
Step 2: Minimize distance errors (method of least squares)
Anchor

## Slide 19: Non Line-of-Sight Propagation
What if the direct path between two nodes is obstructed?
Two nodes are in line-of-sight if:
Node 1
Node 2

## Slide 20: Non Line-of-Sight Propagation
We use the digital compass to get the node orientation
North
Angle of arrival
We can use the digital compass to identify non-line of sight paths
Honeywell HMC6352
Magnetic North

## Slide 21: Outlook: Learning about the Proximity of Nodes
Sampling the received ultrasound signal
  Idea: Identify reflection at nearby obstacles

## Slide 22: Conclusions
SpiderBat platform
  Ultrasound extension board for sensor nodes
  Distance and angle measurements
  Digital compass
Experiments
  Std. dev. of localization error below 5.7 cm (indoor setup)
Non-line of sight propagation
  Detect obstacles between nodes